## Slide 1
Deadline-aware
Foveated Reconstruction
Research weekly update
Network jitter, reconstruction design, and Xavier measurements
2026-10-29
Notes: Weekly update. This deck distinguishes the proposed deadline scheduler from the implemented fixed-center FOV sweep. No measured network jitter or deadline-miss improvement is claimed.

## Slide 2
Jitter reduces the reconstruction budget
2
Later input readiness leaves less time before the display deadline
Early arrival
Budget
Typical arrival
Budget
Late arrival
Budget
Deadline D
Display reserve
Transfer + decode
B = D − t_ready − T_display − margin
Schematic, not a measured jitter trace. A 90 FPS frame period is 11.11 ms, not a validated end-to-end deadline.
Notes: Schematic only, not measured data. 90 FPS gives a frame period of 1000/90=11.11 ms. Frame period is not an established end-to-end deadline. The bars illustrate arrival/decode variability relative to a chosen display deadline.

## Slide 3
Adapt the full-resolution region to available time
3
More time
Larger full-resolution region
Less time
Smaller full-resolution region
Proposed adaptation. Fixed-center levels are measured; scheduling and deadline-miss reduction remain unverified.
Notes: Proposed adaptive mechanism, not implemented/validated. After inputs are ready, more remaining reconstruction time allows a larger full-resolution region; less time calls for a smaller region. The half-resolution base still covers the full image. Region sizes in this schematic are illustrative, not quantitative. Current implementation covers a fixed-center FOV sweep and latency profiles.

## Slide 4
Half-resolution base with a full-resolution center
4
Shared image, disparity, and optical-flow inputs
Base sampling
50% W × 50% H
(25% of pixels)
Base covers the whole image
ROI
+
Full resolution within the ROI
Upsample + blend
960 × 540 output
Full-resolution region: 0.7%, 2.8%, 11.1%, 25.0%, 44.4% of image
Region % means image-area coverage; base sampling is separate. Fixed center, 3 px halo; no eye tracking.
Notes: Source: results/fov_levels_xavier_full_20261027/README.md; overview.csv; summary.csv. Commit 0f1506c. Date 2026-10-27. Raw evidence: evidence.tar.gz. Mechanism: half-resolution base + padded full-resolution ROI + feather overlay. Region percentages are spatial coverage of a 960x540 image: 80x46=0.7098765%, 160x90=2.7777778%, 320x180=11.1111111%, 480x270=25%, 640x360=44.4444444%. The base samples at 50% width and 50% height, giving 25% as many pixels (480x270), while covering the entire image. Region coverage and sampling resolution are different quantities.

## Slide 5
Coverage and measurement scope
5
Forward sequence | Frames | Right-eye frame IDs
15 mm / 300 | 147 | Odd frames 7–299
15 mm / 800 | 387 | Odd frames 7–779
35 mm / 300 | 147 | Odd frames 7–299
35 mm / 800 | 387 | Odd frames 7–779
1068 frames
Xavier 15W Desktop
CUDA 11.4, unlocked clocks
3 warmups + 5 timed runs/frame
One quality output/config/frame
Resident: GPU-resident inputs, reconstruction, upsampling, and blending
Stream: also includes input upload and output download
Excludes backward scenes, even frames, and unsupported tail frames. Timing excludes I/O, allocation, network, decoding, and display.
Notes: Source: results/fov_levels_xavier_full_20261027/README.md; overview.csv; summary.csv. Commit 0f1506c. Date 2026-10-27. Raw evidence: evidence.tar.gz.

## Slide 6
Smaller regions reduce mean reconstruction latency
6
Chart: Mean latency (ms)
| 0.7% | 2.8% | 11.1% | 25.0% | 44.4%
FOV resident | 4.562 | 4.77 | 5.998 | 7.772 | 10.425
FOV stream | 6.364 | 6.728 | 7.839 | 9.655 | 12.193
Full resident | 11.187 | 11.022 | 11.144 | 11.042 | 11.087
2.8% region
4.770 ms
resident mean
2.31×
versus measured full
Fast resampling enabled. Cross-implementation gains also include upsampling changes, not only FOV. No claim of an optimal full baseline.
Notes: Source: results/fov_levels_xavier_full_20261027/README.md; overview.csv; summary.csv. Commit 0f1506c. Date 2026-10-27. Raw evidence: evidence.tar.gz. Arithmetic means of all 5340 timing samples in each level/timing/mode group, computed by compute_means.py into mean_timings.json. No sample trimming. Full baseline measured separately per level. Fast resample enabled. Each value covers all 1068 supported frames. Speedup is mean(full resident)/mean(FOV resident) at the same region level. Region labels are image-area coverage, not sampling resolution.

## Slide 7
Quality–latency trade-off
7
Region (% of image) | Mean latency | Right-eye ΔPSNR | Stereo mean ΔPSNR*
0.7% | 4.562 ms | -0.1727 dB | -0.0864 dB
2.8% | 4.770 ms | -0.1668 dB | -0.0834 dB
11.1% | 5.998 ms | -0.1462 dB | -0.0731 dB
25.0% | 7.772 ms | -0.1200 dB | -0.0600 dB
44.4% | 10.425 ms | -0.0861 dB | -0.0430 dB
* Unchanged left eye, mean per-eye PSNR in dB: stereo difference = right-eye difference / 2
ΔPSNR = FOV − full, using original overflow PSNR. Standard PSNR can show a different trend.
Stereo values are derived; latency is not halved. Non-atomic writes remain. SSIM/LPIPS are not measured.
Notes: Source: results/fov_levels_xavier_full_20261027/README.md; overview.csv; summary.csv. Commit 0f1506c. Date 2026-10-27. Raw evidence: evidence.tar.gz. Original uint8-overflow PSNR preserved. Stereo delta is derived only if left eye remains unchanged and per-eye PSNR dB is averaged. Timing is never divided by two.

## Slide 8
Numba runs on Xavier: a small-sample check
8
Sequence | Full (ms) | Region 2.8% | Region 11.1%
15_300 | 14.661 | 8.924 | 10.304
15_800 | 14.433 | 8.910 | 10.282
35_300 | 14.537 | 8.911 | 10.323
35_800 | 14.567 | 8.959 | 10.372
15W. Frame 39 per sequence, 100 repeats. Preallocated resident-path mean.
Numba 0.58.1 + Python 3.8: real GPU JIT and execution passed.
Its upsampler differs from optimized CUDA C++; this is not a language-only comparison.
Original generate_right also runs with allocation/transfer and startup drift. See the companion deck for 30W.
Notes: Source: results/numba_xavier_20261029/mode7_15w/result.json, environment.txt, run.log. Arithmetic means from mean_timings.json of 100 timing samples per method, four workloads, frame39 only. No confidence intervals. Numba0.58.1/Python3.8/CUDA11.4. Original source-function calls include allocations/transfers/debug copies and show warmup drift; not directly comparable to resident timing.

## Slide 9
Next: measure deadline behavior under jitter
9
1
Record the actual per-frame budget
Log arrival, decode completion, and display deadline. Reserve display time and a margin.
2
Implement budget-based ROI selection
Build a percentile-based profile. Define a fallback when no level fits the budget.
3
Compare fixed and adaptive policies on the same trace
Report deadline-miss rate, tail latency, and quality. Repeat runs to check stability.
Measured: fixed-center quality–latency levels. Adaptive scheduling and benefits under jitter still require validation.
Notes: Proposed future work; no measured jitter trace or deadline-miss reduction exists in the current experiment. All values on earlier slides are local reconstruction measurements, not end-to-end VR results.